## Slide 1
Autonomous and mobile robot for hydroponic greenhouse picking tasks
Candidate
Federico Rollo
ID number 1851121
Thesis Advisor
Prof. Giuseppe Oriolo

## Slide 2: Introduction
Agriculture 4.0:
  new technologies
  the necessity of more products in a minor time.
Different solution have been presented during these years to overcome the population growth.
Use robot to perform hard labour in less time with more productivity
The following work is divided in two main parts:
Feasibility study and design of an algorithm and a robot structure
Simulation and control of the robot to prove the feasibility of the project

## Slide 3: Algorithm

## Slide 4: Greenhouse environment

## Slide 5: Mobile Platform
Three different mobile platform have been considered:
Car-like robot
Differential-drive robot
Mecanum wheels robot

## Slide 6: Car-like robot
Car-like robot
Pro
  Good stability
  Good traction force
Cons
  Difficult to control in narrow passages
  Necessity of maneuvers
Front wheel drive kinematic model

## Slide 7: Differential Drive robot
First configuration → two actuated wheels and an omnidirectional wheel
Differential-drive robot
Pro
  Simple model
  Good controllability
Cons
  Bad stability
Unicycle model
Differential Drive input transformation

## Slide 8: Differential Drive robot
Differential-drive robot
Second configuration → two crawlers
Pro
  Simple model
  Good controllability
  Good stability
  Good traction
Cons
  expensive
Unicycle model
Differential Drive input transformation

## Slide 9: Mecanum wheel robot
Pro
  Omni-directionality
  Good controllability
  Good stability
Cons
  Bad traction on rough terrain
Mecanum wheels robot
Mecanum wheel robot kinematic model

## Slide 10: Mecanum wheel robot
Inverse Kinematic model
Mecanum wheel
Omni-directionality

## Slide 11: Motion Planning

## Slide 12: 6 DOF robotic arm
6 DOF robotic arm has been proven to be enough for picking task
Direct and inverse kinematic studied and also differential kinematic for the control
6 DOF robotic arm

## Slide 13: Vision System
One of the fundamental modules for the picking task.
RGB-D camera choosen based on the ToF tecnology
Recognition, identification and localization of the flowers inside the environment.
Two objectives:
  Flower recognition
  Flower localization
Two algorithm have been developed to accomplish these tasks:
  K-mean algorithm for color clustering
  Moore-Neighbor tracing algorithm modified by Jacob's stopping criteria for flower separation and localization

## Slide 14: Flower identification
Original image
Labeled image
First cluster
Second cluster
Third cluster

## Slide 15: Flower localization
Flower cluster
Binarization, noise attenuation and hole filling
Labeled image
First flower
Second flower
Flower 3D localization

## Slide 16: Robotic arm control
Kinematic control of the robotic arm
Trajectory generation needed for the kinematic control loop input
Trajectory convertion with the robot inverse analitic jacobian
Two contribution for the robot input :
  Feedforward →
  Feedback →

## Slide 17: Trajectory generation
Position path
Orientation path
Final path
Path planning
Timing law

## Slide 18: Existing prototypes
Iron Ox
Sweeper Robot
Root AI
Rubion

## Slide 19: New prototypes – Mobile platform
Dimentions(mm):
400 x 307 x 123
Load capacity:
10kg
Max speed:
0.6m/s
Battery life:
6h
Charging time:
4h
Sensors:
4 ultrasonic
4WD mecanum
Dimentions(mm):
480 x 450 x 134
Load capacity:
20kg
Max speed:
0.6m/s
Battery life:
8h
Charging time:
4h
OMR10
Dimentions(mm):
986 x 662 x 409
Load capacity:
80kg
Max speed:
0.8m/s
Battery life:
7h
Charging time:
5h
Sensors:
2 lidar - 4 ultrasonic
MP-500

## Slide 20: New prototypes – 6 DOF Manipulator arm
RGB sensor:
  Resolution: 1980x1080 at 30fps
Depth sensor
  Resolution:
  480x270 at 30fps
  Min distance: 18cm
Payload:
0.5kg
Max e-e speed:
50 cm/s
Max reach:
706mm
Weight:
5.4kg
Payload:
2kg
Max e-e speed:
50 cm/s
Max reach:
891mm
Weight:
7.2kg
Gen3
Gen3 Light
Kinova RGB-D

## Slide 21: Simulation
Tools
  Matlab & Simulink
  Vrep
The robot mobile platform and its 6 DOF manipulator arm have been developed on Vrep using joints and primitive shapes
Robot modules

## Slide 22: Simulation

## Slide 23: Simulation

## Slide 24: Conclusion
Althought the project has been simplified, the simuation had proven that the algorithms and the structure used works. This project could be applied to a real application scenario in an agriculture 4.0 hydroponic greenhouse.
Future improvements:
  Implement a localization systems
  Improve the machine learning algorithms
  Use multiple robots - distributed systems
  Use a more sophisticated robot controller
  Others

## Slide 25: Acknowledgements
My gratitude goes to my family whose has allowed this moment, my girlfriend who has always supported me and to my university colleagues and professors whose has made this moment possible.
Thank you