## Slide 1
Autonomous and mobile robot for hydroponic greenhouse picking tasks
Candidate
Federico Rollo
ID number 1851121
Thesis Advisor
Prof. Giuseppe Oriolo

## Slide 2: Introduction
Agriculture 4.0:
  new technologies
  the necessity of more products in a minor time.
Different solutions presented during these years to overcome population growth.
Use of robots to perform hard labor in less time with more productivity

## Slide 3: Case of study
Development of a zucchini flower picking robot for the SolarFields hydroponic greenhouses.
SolarFields company is a clean energy productor which is investing in hydroponic greenhouse start-ups like Idroluppolo
These companies are working together to find healthy solution to provide fresh and biological fruits on the market
Robotics and automation aims to make the production processes fully autonomous

## Slide 4: Existing robots
Iron Ox
Sweeper Robot
Root AI
Rubion

## Slide 5: Project specifications
The robot is composed of three main parts:
  Mobile platform
  Robotic arm
  Vision system
The aim of the robot is to move inside the greenhouse and pick the zucchini flowers on the plants
The following work is divided in two main parts:
Feasibility study and design of algorithm and robot structure
Simulation and control of the robot to prove the project feasibility

## Slide 6: Algorithm

## Slide 7: Greenhouse environment

## Slide 8: Mobile Platform
Three different mobile platforms have been considered:
Car-like robot
Differential drive robot
Mecanum wheels robot

## Slide 9: Car-like robot
Car-like robot
Pro
  Good stability
  Good traction force
Cons
  Difficult to control in narrow passages
  Necessity of maneuvers
Front wheel drive kinematic model

## Slide 10: Differential drive robot
First configuration → two actuated wheels and an omnidirectional wheel
Differential drive robot
Pro
  Simple model
  Good controllability
Cons
  Bad stability due to manipulator arm attached on
Unicycle model
Differential drive input transformation

## Slide 11: Differential drive robot
Second configuration → two actuated crawler
Differential drive robot
Pro
  Simple model
  Good controllability
  Good stability
  Good traction
Cons
  Expensive
Unicycle model
Differential drive input transformation

## Slide 12: Mecanum wheel robot
Pro
  Omni-directionality
  Good controllability
  Good stability
Cons
  Bad traction on rough terrain
Mecanum wheels robot
Mecanum wheel robot kinematic model

## Slide 13: Mecanum wheel robot
Inverse kinematic model
Mecanum wheel
Omni-directionality

## Slide 14: Mobile platform prototypes
Dimensions(mm):
400 x 307 x 123
Load capacity:
10kg
Max speed:
0.6m/s
Battery life:
6h
Charging time:
4h
Sensors:
4 ultrasonic
4WD mecanum
Dimensions(mm):
480 x 450 x 134
Load capacity:
20kg
Max speed:
0.6m/s
Battery life:
8h
Charging time:
4h
OMR10
Dimensions(mm):
986 x 662 x 409
Load capacity:
80kg
Max speed:
0.8m/s
Battery life:
7h
Charging time:
5h
Sensors:
2 lidar - 4 ultrasonic
MP-500

## Slide 15: Trajectory planning and control

## Slide 16: 6 DOF robotic arm
6 DOF robotic arm has been proven to be enough for the picking task
The forward and inverse kinematics have been computed for simulation purposes using Denavit-Hartemberg convention
The differential kinematics has been derived by the forward kinematics and it has been used for the robot control
6 DOF robotic arm

## Slide 17: 6 DOF Manipulator arm prototypes
Payload:
0.5kg
Max e-e speed:
50 cm/s
Max reach:
706mm
Weight:
5.4kg
Gen3
Payload:
2kg
Max e-e speed:
50 cm/s
Max reach:
891mm
Weight:
7.2kg
Gen3 Light
RGB sensor:
  Resolution: 1980x1080 at 30fps
Depth sensor
  Resolution:
  480x270 at 30fps
  Min distance: 18cm
Kinova RGB-D

## Slide 18: Vision System
One of the fundamental modules for the picking task.
RGB-D camera chosen based on the ToF technology
Recognition, identification and localization of the flowers inside the environment.
Two objectives:
  Flower recognition
  Flower separation and localization
Two algorithm have been developed to accomplish these tasks:
  K-mean algorithm for color clustering
  Moore-Neighbor tracing algorithm modified by Jacob's stopping criteria for flower separation

## Slide 19: Flower identification
Original image
Labeled image
First cluster
Second cluster
Third cluster

## Slide 20: Flower separation and localization
Flower cluster
Binarization, noise attenuation and hole filling
Labeled image
First flower
Second flower
Flower 3D localization

## Slide 21: Trajectory generation
Position path
Orientation path
Final path
Path planning
Timing law

## Slide 22: Robotic arm kinematic control
A kinematic controller has been used to control the robot
The input of the control loop is the cartesian speed trajectory of the robot’s end-effector
The trajectory is converted from the speed cartesian space to the speed joint space using the robot inverse analytic Jacobian
Two contribution for the robot input:
  Feedforward →
  Feedback →

## Slide 23: Simulation
Tools
  Matlab
  Vrep
The robot mobile platform and its 6 DOF manipulator arm have been developed on Vrep using joints and primitive shapes

## Slide 24: Simulation

## Slide 25: Simulation

## Slide 26: Conclusion
Although the project has been simplified, the simulation had proven that the algorithms and the structure used works. This project could be applied to a real application scenario in an agriculture 4.0 hydroponic greenhouse.
Future improvements:
  Implement a localization systems
  Improve the machine learning algorithms
  Use multiple robots - distributed systems
  Use a more sophisticated robot controller